## Slide 1: Operating System
Chapter 11 I/O Management and Disk Scheduling

## Slide 2: Chapter 11 I/O Management and Disk Scheduling
11.1 I/O Devices
11.2 Organization of the I/O Function
11.3 Operating System Design Issues
11.4 I/O Buffering
11.5 Disk Scheduling
11.6 RAID
11.7 Disk Cache
11.8 Summary

## Slide 3: 11.1 I/O Devices(1/6)
Categories of I/O Devices(I/O设备分类)
  1. Human readable(人可读)
    Used to communicate with the user
    Printers
    Video display terminals
    Display
    Keyboard
    Mouse

## Slide 4: 11.1 I/O Devices(2/6)
Categories of I/O Devices
  2. Machine readable(机器可读)
    Used to communicate with electronic equipment
    Disk drives
    Sensors
    Controllers
    Tape drives
    Actuators

## Slide 5: 11.1 I/O Devices(3/6)
Categories of I/O Devices
  3. Communication(通信)
    Used to communicate with remote devices
    Digital line drivers
    Modems
    Network device

## Slide 6: 11.1 I/O Devices(4/6)
Differences in I/O Devices
  1. Data rate：May be differences of several orders of magnitude(数量级) between the data transfer rates

## Slide 7: 11.1 I/O Devices(5/6)
Differences in I/O Devices
  2. Application-specific
    Disk used to store files requires file management software
    Disk used to store virtual memory pages needs special hardware and software to support it
    Terminal used by system administrator may have a higher priority
  3. Complexity of control

## Slide 8: 11.1 I/O Devices(6/6)
Differences in I/O Devices
  4. Unit of transfer
    Data may be transferred as
      a stream of bytes，e.g. terminal
      in larger blocks, e.g. disk
  5. Data representation
    Encoding schemes
  6. Error conditions
    Devices respond to errors differently

## Slide 9: Chapter 11 I/O Management and Disk Scheduling
11.1 I/O Devices
11.2 Organization of the I/O Function
11.3 Operating System Design Issues
11.4 I/O Buffering
11.5 Disk Scheduling
11.6 RAID
11.7 Disk Cache
11.8 Summary

## Slide 10: 11.2 Organization of the I/O Function
11.2.1 Techniques for Performing I/O
11.2.2 Evolution of the I/O Function
11.2.3 Direct Memory Access

## Slide 11: 11.2.1 Techniques for Performing I/O(1/4)
1. Programmed I/O(可编程I/O)
  Programmed I/O happens when software running on the CPU uses instructions that access I/O address space to perform data transfers to or from an I/O device.
    Each data item transfer is initiated by an instruction in the program.
  In Programmed I/O processor executes a program that gives the direct control of I/O operation.
  Process is busy-waiting for the operation to complete.

## Slide 12: 11.2.1 Techniques for Performing I/O(2/4)
2. Interrupt-driven I/O(中断驱动I/O)
  I/O command is issued
  Processor continues executing instructions
  I/O module sends an interrupt when done
  Asking for a input from the user would be an interrupt-driven I/O.
Notes: PIO often uses an interrupt (from the device) to initiate each byte/word data transfer. This helps mitigate the CPU-intensive nature of PIO. A polled PIO transfer would otherwise totally consume CPU resources.

## Slide 13: 11.2.1 Techniques for Performing I/O(3/4)
3. Direct Memory Access (DMA,直接存储器访问)
  DMA module controls exchange of data between main memory and the I/O device
  Processor interrupted only after entire block has been transferred.
  DMA's are mostly used when there is a demand of frequent transfer of big chunk of data.

## Slide 14: 11.2.1 Techniques for Performing I/O(4/4)
Relationship Among Techniques

## Slide 15: 11.2 Organization of the I/O Function
11.2.1 Techniques for Performing I/O
11.2.2 Evolution of the I/O Function
11.2.3 Direct Memory Access

## Slide 16: 11.2.2 Evolution of the I/O Function(1/2)
1. Processor directly controls a peripheral device
  Processor has to handle details of external devices
2. Controller or I/O module is added
  Processor uses programmed I/O without interrupts
  Processor does not need to handle details of external devices
3. Controller or I/O module with interrupts
  Processor does not spend time waiting for an I/O operation to be performed

## Slide 17: 11.2.2 Evolution of the I/O Function(2/2)
4. Direct Memory Access
  Blocks of data are moved into memory without involving the processor
  Processor involved at beginning and end only
5. I/O channel
  I/O module is to a separate processor
  The central processing unit (CPU) directs the I/O processor to execute an I/O program in main memory.
6. I/O processor
  I/O module is a processor with its own local memory
  It's a computer in its own right

## Slide 18: 11.2 Organization of the I/O Function
11.2.1 Techniques for Performing I/O
11.2.2 Evolution of the I/O Function
11.2.3 Direct Memory Access

## Slide 19: 11.2.3 Direct Memory Access(1/6)
What is Direct Memory Access(直接存储器访问)?
  Hardware mechanism that allows peripheral components to transfer their I/O data directly to and from main memory without the need to involve the system processor.
Why is Direct Memory Access important?
  Use of this mechanism can greatly increase throughput to and from a device, because a great deal of computational overhead is eliminated

## Slide 20: 11.2.3 Direct Memory Access(2/6)
Hardware using DMA
  disk drives, graphics cards, network cards, sound cards
What is the downside?
  Hardware support is required – DMA controllers
  DMA “steals” cycles (周期挪用) from the processor
    The instruction cycle is suspended so data can be transferred o the system bus
    The CPU pauses one bus cycle
    No interrupts occur, does not need to save context
  Synchronization mechanisms must be provided to avoid accessing non-updated information from RAM

## Slide 21: 11.2.3 Direct Memory Access(3/6)
Process of DMA

## Slide 22: 11.2.3 Direct Memory Access(4/6)
Typical DMA block diagram
Notes: DMA既可以指内存和外设直接存取数据这种内存访问的计算机技术，又可以指实现该技术的硬件模块（对于通用计算机PC而言，DMA控制逻辑由CPU和DMA控制接口逻辑芯片共同组成，嵌入式系统的DMA控制器内建在处理器芯片内部，一般称为DMA控制器，DMAC）。
一般而言，DMA控制器将包括一条地址总线、一条数据总线和控制寄存器。高效率的DMA控制器将具有访问其所需要的任意资源的能力，而无须处理器本身的介入，它必须能产生中断。最后，它必须能在控制器内部计算出地址。

## Slide 23: 11.2.3 Direct Memory Access(5/6)
DMA Transfer

## Slide 24: 11.2.3 Direct Memory Access(6/6)
DMA Configurations

## Slide 25: Chapter 11 I/O Management and Disk Scheduling
11.1 I/O Devices
11.2 Organization of the I/O Function
11.3 Operating System Design Issues
11.4 I/O Buffering
11.5 Disk Scheduling
11.6 RAID
11.7 Disk Cache
11.8 Summary

## Slide 26: 11.3 Operating System Design Issues
Efficiency and generality are most important objectives in designing the I/O facility

## Slide 27: 11.3 Operating System Design Issues
Efficiency (效率)
  Most I/O devices extremely slow compared to main memory
    Use of multiprogramming(多道程序) allows for some processes to be waiting on I/O while another process executes
    I/O cannot keep up with processor speed
    Swapping(交换) is used to bring in additional Ready processes which is an I/O operation
Optimise I/O efficiency – especially Disk & Network I/O

## Slide 28: 11.3 Operating System Design Issues
Generality (通用性)
  Desirable to handle all I/O devices in a uniform manner(统一模式)
    Both in the OS and in user applications
  Hide most of the details of device I/O in lower-level routines so that processes and upper levels see devices in general terms such as read, write, open, close, lock, unlock

## Slide 29: 11.3 Operating System Design Issues

## Slide 30: 11.3 Operating System Design Issues
Layers of the I/O Software System

## Slide 31: 11.3 Operating System Design Issues
Layers of the I/O system and the main functions of each layer

## Slide 32: 11.3 Operating System Design Issues
Device-Independent I/O Software
  Drivers use a defined interface to kernel services (e.g. kmalloc, install IRQ handler, etc.)
  Allows kernel to evolve without breaking existing drivers
(a) Without a standard driver interface (b) With a standard driver interface

## Slide 33: Chapter 11 I/O Management and Disk Scheduling
11.1 I/O Devices
11.2 Organization of the I/O Function
11.3 Operating System Design Issues
11.4 I/O Buffering
11.5 Disk Scheduling
11.6 RAID
11.7 Disk Cache
11.8 Summary

## Slide 34: 11.4 I/O Buffering
Reasons for buffering(缓存原因)
  Processes must wait for I/O to complete before proceeding
  Certain pages must remain in main memory during I/O
Define of I/O buffering
  Performs input transfers in advance of requests being made and performs output transfers some time after the request is made(预输入，缓输出)

## Slide 35: 11.4 I/O Buffering
Block-oriented(面向块)
  Information is stored in fixed sized blocks
  Transfers are made a block at a time
  Used for disks and tapes
Stream-oriented(面向流)
  Transfers information as a stream of bytes
  Used for terminals, printers, communication ports, mouse and other pointing devices, and most other devices that are not secondary storage

## Slide 36: 11.4 I/O Buffering
Single Buffer(单缓冲)
  Operating system assigns one buffer in the system space for an I/O request
  Block-oriented single buffering
    Input transfers are made to buffer
    Block is moved to user space when needed
    Another block is requested immediately
      Read ahead(预读), or anticipated input(预输入)

## Slide 37: 11.4 I/O Buffering
Block-oriented single buffer
  Advantages
    User process can process one block of data while next block is read in
    Swapping can occur since input is taking place in system memory, not user memory
  Disadvantages
    Operating system keeps track of assignment of system buffers to user processes
    The swapping logic is affected

## Slide 38: 11.4 I/O Buffering
Stream-oriented single buffer
  Line-at-a-time fashion
    Input from or output to a terminal is one line at a time with carriage return signaling the end of the line
  Bye-at-a-time fashion
    Input and Output follow the producer/consumer model

## Slide 39: 11.4 I/O Buffering
Single Buffer
  Computation and transfer can be done in parallel
  Speed up with buffering:
Assume
T is transfer time for a block from device
C is computation time to process incoming block
M is time to copy kernel buffer to user buffer

## Slide 40: 11.4 I/O Buffering
Double Buffer(双缓冲)
  Use two system buffers instead of one
  Computation and Memory copy can be done in parallel with transfer
Speed up with double buffering：
  Usually M is much less than T giving a favourable result

## Slide 41: 11.4 I/O Buffering
Circular Buffer(循环缓冲)
  More than two buffers are used
  Each individual buffer is one unit in a circular buffer
  Used when I/O operation must keep up with process

## Slide 42: Chapter 11 I/O Management and Disk Scheduling
11.1 I/O Devices
11.2 Organization of the I/O Function
11.3 Operating System Design Issues
11.4 I/O Buffering
11.5 Disk Scheduling
11.6 RAID
11.7 Disk Cache
11.8 Summary

## Slide 43: 11.5 Disk Scheduling
11.5.1 Disk Performance Parameters
11.5.2 Disk Scheduling Policies

## Slide 44: 11.5.1 Disk Performance Parameters(1/6)
To read or write, the disk head must be positioned at the desired track(磁道) and at the beginning of the desired sector(扇区)

## Slide 45: 11.5.1 Disk Performance Parameters(2/6)
Seek time (寻道时间)
  Time it takes to position the head(磁头) at the desired track
Notes: Seek times describes the time it takes to position the read/write heads radially across the platter. The following specifications are often published: Full Stroke - the time it takes to move across the entire width of the disk, from the innermost track to the outermost. Average – the average time it takes to move from one random track to another (normally listed as the time for one-third of a full stroke). Track-to-Track – the time it takes to move between adjacent tracks.
Each of these specifications is measured in milliseconds (ms).

## Slide 46: 11.5.1 Disk Performance Parameters(3/6)
Rotational delay
  Time its takes for the beginning of the sector to reach the head.
    Rotational latency is dependent upon the rotation speed of the spindle 、
    measured in milliseconds (ms)
Notes: The actuator moves the read/write head over the platter to a particular track, while the platter spins to position the a particular sector under the read write head.
Rotational latency is the time that it takes the platter to rotate and position the data under the read/write head.
  Rotational latency is dependent upon the rotation speed of the spindle and is measured in milliseconds (ms)
  The average rotational latency is one-half of the time taken for a full rotation.
  Like seek times, rotational latency has more of an impact on reads or writes of random sectors on the disk than on the same operations on adjacent sectors.
Instructor note: rotational latency is around 5.5 ms for a 5,400 rpm drive, and around 2.0 ms for a 15,000 rpm drive.

## Slide 47: 11.5.1 Disk Performance Parameters(4/6)
Timing of a Disk I/O Transfer

## Slide 48: 11.5.1 Disk Performance Parameters(5/6)
Access time(存取时间)
  The time it takes to get in position to read or write
  Sum of seek time (Ts) and rotational delay (1/2r)
Transfer time(传输时间, b/(rN) )
  Data transfer occurs as the sector moves under the head
Thus the total average access time can be expressed as:
Ta：总平均存取时间, total average access time
Ts：平均寻道时间, aversage seeking time
r：旋转速度，转/秒, $ rotation speed, in revolutions per second
b：要传送字节数,number of bytes to be transferred
N：一个磁道的字节数, number of bytes on a track

## Slide 49: 11.5.1 Disk Performance Parameters(6/6)
Sequential access:
    Total time = 16+(4x12)=64ms
  Random access
    Total time = 2500 * 8.016 = 20,040 ms
5 adjacent tracks, 500 sectors/track, total 2500 sectors
It is clear that the order in which sectors are read from the disk has a tremendous effect on I/O performance.

## Slide 50: 11.5 Disk Scheduling
11.5.1 Disk Performance Parameters
11.5.2 Disk Scheduling Policies

## Slide 51: 11.5.2 Disk Scheduling Policies(1/10)
Seek time and rotational delay are the reasons for differences in performance
  The key to increase performance of disk is to minimize seek time
Random scheduling
  For a single disk there will be a number of I/O requests
  It gives poor performance
  Used to evaluate other techniques

## Slide 52: 11.5.2 Disk Scheduling Policies(2/10)
First-in, first-out (FIFO)
  Process request sequentially
  Fair to all processes
  Approaches random scheduling in performance if there are many processes
55、58、39、18、90、160、150、38、184

## Slide 53: 11.5.2 Disk Scheduling Policies(3/10)
Priority(PRI 优先级)
  Not intended to optimize disk utilization but to meet other objectives
  Short batch jobs may have higher priority
  Provide good interactive response time
  This type of policy tends to be poor for database systems.

## Slide 54: 11.5.2 Disk Scheduling Policies(4/10)
Last-in, first-out (LIFO)
  Good for transaction processing systems
    The device is given to the most recent user so there should be little arm movement
  Possibility of starvation since a job may never regain the head of the line

## Slide 55: 11.5.2 Disk Scheduling Policies(5/10)
Shortest Service Time First (SSTF)
  Select the disk I/O request that requires the least movement of the disk arm from its current position
  Always choose the minimum Seek time
55、58、39、18、90、160、150、38、184

## Slide 56: 11.5.2 Disk Scheduling Policies(6/10)
SCAN
  Arm moves in one direction only, satisfying all outstanding requests until it reaches the last track in that direction
  Direction is reversed
55、58、39、18、90、160、150、38、184

## Slide 57: 11.5.2 Disk Scheduling Policies(7/10)
C-SCAN (circular SCAN)
  Restricts scanning to one direction only
  When the last track has been visited in one direction, the arm is returned to the opposite end of the disk and the scan begins again
55、58、39、18、90、160、150、38、184

## Slide 58: 11.5.2 Disk Scheduling Policies(8/10)
N-step-SCAN
  Segments the disk request queue into subqueues of length N
  Subqueues are processed one at a time, using SCAN
  New requests added to other queue when queue is processed
FSCAN
  Two queues
  One queue is empty for new requests

## Slide 59: 11.5.2 Disk Scheduling Policies(9/10)

## Slide 60: 11.5.2 Disk Scheduling Policies(10/10)

## Slide 61: Chapter 11 I/O Management and Disk Scheduling
11.1 I/O Devices
11.2 Organization of the I/O Function
11.3 Operating System Design Issues
11.4 I/O Buffering
11.5 Disk Scheduling
11.6 RAID
11.7 Disk Cache
11.8 Summary

## Slide 62: 11.6 RAID(1/5)
Redundant Array of Independent Disks (独立冗余磁盘阵列) or Redundant Array of Inexpensive (廉价冗余磁盘整列)
Set of physical disk drives viewed by the operating system as a single logical drive
Redundancy is used to improve reliability.
The RAID scheme consists of seven levels, zero through six.
Notes: 组成磁盘阵列的不同方式称为RAID Level

## Slide 63: 11.6 RAID(2/5)
RAID 0 (non-redundant)
  The data are striped across the available disks
  RAID 0 splits data evenly across two or more disks, without parity information, redundancy, or fault tolerance.
  High data transfer capacity

## Slide 64: 11.6 RAID(3/5)
RAID 1 (mirrored 磁盘镜像)
  RAID 1 consists of an exact copy of a set of data on two or more disks.
  This means that when you write a file, the file is actually written to two disks. If one of the disks fails, you simply replace it and rebuild the mirror.
  The tradeoff with RAID 1 is cost.

## Slide 65: 11.6 RAID(4/5)
RAID 3 (bit-interleaved parity)
  rarely used in practice
  consists of byte-level striping with a dedicated parity disk（专有校验磁盘）.
Notes:   One of the characteristics of RAID 3 is that it generally cannot service multiple requests simultaneously, which happens because any single block of data will, by definition, be spread across all members of the set and will reside in the same physical location on each disk.
  Therefore, any I/O operation requires activity on every disk and usually requires synchronized spindles.

## Slide 66: 11.6 RAID(5/5)
RAID 5
  A standard RAID level configuration that uses block-level data striping and distributes parity to all the disks.
  It is currently one of the most commonly used RAID methods.

## Slide 67: Chapter 11 I/O Management and Disk Scheduling
11.1 I/O Devices
11.2 Organization of the I/O Function
11.3 Operating System Design Issues
11.4 I/O Buffering
11.5 Disk Scheduling
11.6 RAID
11.7 Disk Cache
11.8 Summary

## Slide 68: 11.7 Disk Cache(1/3)
Buffer in main memory for disk sectors
Contains a copy of some of the sectors on the disk
Two design issues:
  Method to transfer the block of data from the disk cache to memory assigned to the user process(缓存数据与用户空间交换)
    Data move
    Pointer passing
  The replacement strategy(置换策略) when the disk cache is full for store new data

## Slide 69: 11.7 Disk Cache(2/3)
Replacement Strategy 1: Least Recently Used (最近最少使用)
  The block that has been in the cache the longest with no reference to it is replaced
  The cache consists of a stack of blocks
  Most recently referenced block is on the top of the stack
  When a block is referenced or brought into the cache, it is placed on the top of the stack
  The block on the bottom of the stack is removed when a new block is brought in
  Blocks don't actually move around in main memory，A stack of pointers is used

## Slide 70: 11.7 Disk Cache(3/3)
Replacement Strategy 2: Least Frequently Used (最不常用)
  The block that has experienced the fewest references is replaced
  A counter is associated with each block
  Counter is incremented each time block accessed
  Block with smallest count is selected for replacement

## Slide 71: Chapter 11 I/O Management and Disk Scheduling
11.1 I/O Devices
11.2 Organization of the I/O Function
11.3 Operating System Design Issues
11.4 I/O Buffering
11.5 Disk Scheduling
11.6 RAID
11.7 Disk Cache
11.8 Summary

## Slide 72: Question #1：课堂1题
There is sequence of disk track requests:96 58 82 36 168 130 150 25 184.
Assume that the disk head
  is initially positioned over track 100
  and is moving in the direction of increasing track number.
Question: For FIFO/SSTF/SCAN/C-SCAN
  What is the tracking order?
  What is Average Track Length?

## Slide 73: Assignment: 课后两题
Question #1：课后习题11.3
Question #2：There is sequence of disk track requests:75 62 99 144 50 162 110 26 198.
Assume that the disk head
  is initially positioned over track 100
  and is moving in the direction of decreasing track number.
For FIFO/SSTF/SCAN/C-SCAN
  What is the tracking order?
  What is Average Track Length?